## Slide 1: Creative Camera Techniques
Depth of Field
Notes: Example of deep depth of field
HAVE TO CLICK TO BRING UP THE CAPTION
Everything in focus, gives a clear bright mood

## Slide 2: Depth of Field
What is Depth of Field?
The distance both in front of and behind the focus point which appears acceptably focused.
Notes: HAVE TO CLICK TO BRING UP DOF GRAPHIC

## Slide 3: Depth of Field
Deep
FL 35 mm
Focus 50 m
f 16
http://www.diyphotography.net/aperture
Everything in focus…bright mood

## Slide 4: Depth of Field
Shallow
Nikon DX
FL ~200 mm
Focus ~40 m
f 4
Shallow Depth of Field: Draws eye to the subject

## Slide 5: Depth of Field
Shallow
Nikon D90
(DX format)
FL 105 mm
Focus ~3.2 cm
f 10

## Slide 6: Depth of Field
Shallow
FL 100 mm
Focus ~1.5 m
f 2.8

## Slide 7: Depth of Field
Shallow
Canon 30D (APS-C)
FL 50 mm
Focus ~1.5 m
f 5

## Slide 8: Depth of Field
Shallow
FL 100 mm
Focus ~3 m
f 2.8
Blurred background produces a soft mood.

## Slide 9: Depth of Field
Shallow
FL 200 mm
Focus ~15 m
f 4
http://www.lyitdesign.com/phpBB3/viewtopic.php?f=5&t=18
Be careful when using a shallow depth of field that there is not a bright area behind the subject which competes with the subject.
Subject is isolated from the background.

## Slide 10: Depth of Field
Depth of Field too deep:
No separation of shore and boats.
Subject unclear.

## Slide 11: Depth of Field

## Slide 12: Depth of Field
Shallow depth of field
Correct focus
Subject clearly defined
PERFECT! (almost)

## Slide 13: Depth of Field
Camera Controls of Depth of Field:
Focus Distance:
  a. The closer the focus the shallower the Depth of Field. (Focal length constant). Affects composition.
2. Lens Focal Length:
  a. The longer the focal length the shallower the Depth of Field. (Focus distance constant). Affects composition.
3. Aperture:
  The larger the aperture number, the deeper the Depth of Field. This is the only control which does not affect composition.
Depth of Field Calculator (computer): http://www.dofmaster.com/dofjs.html
iPhone app: “SetMyCamera”
  c. Convenient to set camera on Aperture Priority mode (‘Av’ Canon, ‘A’ Nikon)

## Slide 14: Creative Camera Techniques
Motion
Contrast between blurry images and the clear image draws attention to the clear subject.
A stationary person on a busy street gives the feeling of motion: moving in a crowd of people.
Notes: Example of deep depth of field
HAVE TO CLICK TO BRING UP THE CAPTION
Everything in focus, gives a clear bright mood

## Slide 15
Motion
Notes: Example of deep depth of field
HAVE TO CLICK TO BRING UP THE CAPTION
Everything in focus, gives a clear bright mood

## Slide 16
Motion
Blurred image gives the feeling of movement
Notes: Example of deep depth of field
HAVE TO CLICK TO BRING UP THE CAPTION
Everything in focus, gives a clear bright mood

## Slide 17
Motion
Contrast with
Blurred image gives better feeling of motion.
Notes: Example of deep depth of field
HAVE TO CLICK TO BRING UP THE CAPTION
Everything in focus, gives a clear bright mood

## Slide 18: Creative Camera Techniques
Motion
Camera Controls of Motion:
  Lens focal length: The longer the focal length the easier to create blur. Affects composition.
  Shutter Speed: the longer the shutter speed the easier to create blur.
  No effect on composition.
  Use Shutter Priority Mode (‘Tv’ Canon, ‘S’ Nikon)
Notes: Example of deep depth of field
HAVE TO CLICK TO BRING UP THE CAPTION
Everything in focus, gives a clear bright mood

## Slide 19
Motion
Considerations:
  Bright Day: requires a fast shutter speed. No problem to stop motion.
    Problem: To create blur requires a slow shutter speed.
      Increase the aperture number
      Decrease the ISO.
        (For best image quality use the native ISO for your camera.)
      Use a neutral density filter (polarizing filter).
  Dark environment: requires a slow shutter speed. No problem to create blur.
    Problem: to stop action requires a fast shutter.
      Use a smaller aperture number. Trade sharpness for shallow depth of field.
      Increase the ISO. Trade sharpness for noise.
      Use a tripod. Will stop camera shake blur but will not stop subject motion blur.
      Use a flash. On camera flash causes a flat pasted look. Off camera flash done well is extremely effective.
  Most convenient way to control shutter speed is to use Shutter Priority: you set the shutter speed, the camera sets the aperture.
Notes: Example of deep depth of field
HAVE TO CLICK TO BRING UP THE CAPTION
Everything in focus, gives a clear bright mood

## Slide 20
Exposure
Exposure Control:
Putting it all together:
The Exposure Triangle
ISO
Shutter
Aperture
Noise
Motion Blur
Depth of Field
The exposure triangle contains all of the exposure functions:
Each function plays a role in the final image.
Exposure triangle provides a rational for exposure settings.

## Slide 21
Exposure
Exposure Control:
Putting it all together cont:
Examples
Slow shutter
Large aperture #
Fast shutter
Small aperture #
Panning
Medium shutter
Medium aperture
Fast shutter
Small aperture #

## Slide 22
Taking the Picture…
1. Is this an action image or a depth of field image?
  Action: use shutter priority mode (‘Tv’ Canon, ‘S’ Nikon)
    Stop action: use fast shutter speed,
    Blur action: use slow shutter
  Depth of field: use aperture priority mode (‘Av’ Canon, ‘A’ Nikon)
    Shallow depth of field: use a small aperture number
    Deep depth of field: use a large aperture number
  Is the shutter speed high enough (for hand holding)?
    Use a tripod
    Increase ISO
  Very fast action: consider continuous shooting mode with continuous focus.
Is this an unusual lighting situation? Use exposure compensation?
  Bright, low contrast: need to “over expose”
  Dark, low contrast: need to “under expose”
  Bracket?
Compose the image. Check focus
Click!
Assess the scene and imagine the image
(pre-event visit)